ICM Development in HAPS
Interference Coordination Method
for Integrated HAPS-Terrestrial Networks

---
The Speakers
The Speakers
Potsawat Thinkanwatthana
6410451199
potsawat.t@ku.th
Sornsiri Hongsa
6410451431
sornsiri.h@ku.th

---
Outline
Outline
1. HAPS, Terrestrial Networks, and Their System Model
2. Interference Analysis
3. Proposed Interference Coordination Method
4. Evaluation Results
5. Conclusions
6. Our Thoughts
7. Q&A

---
HAPS
HAPS
- High Altitude Platform Station
- HAPS can be any Unmanned Aerial Vehicle (UAV) that fly or float in the stratosphere
- Typically at altitudes of around 20 km.
- HAPS system use solar power or an on-board energy source

---
Terrestrial Networks (TN)
Terrestrial Networks (TN)
- Ground-based cellular networks.
- Terrestrial networks consist of terrestrial base stations which randomly distributed within the coverage area of HAPS.

---
System Model of HAPS
System Model of HAPS
Case 1 - HAPS provides services for customer premise equipment (CPE) or terrestrial base stations (BS) on the ground and CPE/BS provide mobile services for user equipment (UE)

---
System Model of HAPS
System Model of HAPS
Case 2 - HAPS directly provides mobile services for UE on the ground

---
System model of TN
System model of TN
Terrestrial networks have path loss and shadow fading, which are influenced by the scenario configuration
Terrestrial Base Station can use fully dynamic beamforming and precoding schemes for better performance

---
Interference Analysis
Interference Analysis
The highlight of interference in integrated system is the interference from HAPS downlink to terrestrial downlink, especially to user equipment (UE)
Multi-beam transmission in HAPS can cause inter-beam interference. And its will lead to intra-beam interference.
This method goals is to achieve better resource utilization and performance by dynamically considering the changing traffic load in HAPS and terrestrial networks

---
Interference Analysis
Interference Analysis

---
The Proposed Method
The Proposed Method

---
Traffic Load and Deployment
Traffic Load and Deployment
Different cases based on traffic distribution and deployment
of integrated system
Liu, W., Hou, X., Chen, L., Hokazono, Y., & Zhao, J. (2022). Interference Coordination Method for Integrated HAPS-Terrestrial Networks. 2022 IEEE 95th Vehicular Technology Conference: (VTC2022-Spring). https://doi.org/10.1109/vtc2022-spring54318.2022.9860546

---
Case A: Non-overlapping Areas
Case A: Non-overlapping Areas
- No overlaps between HAPS and TN coverage,
  only HAPS coverage is provided
- No interference

---
Case Bs: Overlapping Areas
Case Bs: Overlapping Areas
- Their exist overlapping areas between HAPS and TN coverage
- Considering traffic distribution in HAPS and TN, this case is further divided into 3 subcases, B1 through B3

---
B-subcases
B-subcases
Subcase	Traffic Load	Condition	Consideration
B1	HAPS	Inter-system interference can be ignored; long distance between HAPS and TN	Turn TN base stations into idle state
B2	TN	No interference from HAPS to TN	Turn HAPS beam or CPE for the cell off
B3	HAPS and TN	Inter-beam interference from HAPS cells / Inter-system interference	Further analysis required (next page)

---
Case B3 Analysis: The Patterns
Case B3 Analysis: The Patterns
Pattern #	HAPS is active	TN is active	Coordination
1	✔	✔	✗ Both HAPS and TN serve users with same time-frequency resources
2	✔	✔	✔
3	✗	✔	✗
4	✔	✗	✗

---
Evaluation Results
Evaluation Results
Result	Proposed Method	Baseline 1 / (Fixed Allocation)	Baseline 2 / (Orthogonal Allocation)
Throughput / (HAPS Users)	Higher	Lower	Higher
Throughput / (Terrestrial Users)	Higher	Higher	Lower
Interbeam Interference	Mitigated	Ignored	Significant

---
Evaluation Results
Evaluation Results

---
Conclusions
Conclusions
To coordinate HAPS and TN, we must take into account the inter-system interference.
The paper shows possible scenarios and proposed a method that can be used to determine the optimized pattern for distributing traffic between the two systems. The optimized pattern is the pattern such that throughput is at its maximum and is subject to the minimum data rate requirement.
The evaluation results show that this method improves performance by maximizing throughput when comparing to the current HAPS architecture.

---
Our Thoughts: Potsawat
Our Thoughts: Potsawat
The ICM method does help improve efficiency and traffic optimization between HAPS and TNs by distributing workload between the two.
Nevertheless, the evaluation results show that this method majorly covers particular regions with particular distance from HAPS cells. This may also mean the increased implementation cost in order to fairly provide service to users across a coverage area.
HAPS is meant to both improve performance, and reduce implementation and maintenance cost.

---
Our Thoughts: Sornsiri
Our Thoughts: Sornsiri
The primary consideration from this paper is the reduction of resources used for data exchange in each time.
If this issues can be fixed, not only HAPS but the overall efficiency of the terrestrial network (NTN) will improve significantly.
This method could potentially lead to the development of 5G and 6G signal networks in the future.

---
References
References
[1] Wenjia Liu and others. “Interference Coordination Method for Integrated HAPS-Terrestrial Networks”. in 2022 IEEE 95th Vehicular Technology Conference: (VTC2022-Spring): 2022, pages 1–6. DOI: 10.1109/VTC2022-Spring54318.2022.9860546.
[2] GSMA. High Altitude Platform Systems. Tower in the Skies. version 2.0. 2022.

---
Q&A